## Slide 1
ViMMS: A Digital Twin of a Metabolomics Mass Spectrometer
Dr Vinny Davies

## Slide 2
Metabolomics is the "systematic study of the unique chemical fingerprints that specific cellular processes leave behind", the study of their small-molecule metabolite profiles.
Basically, we are trying to identify all the metabolites in a particular sample
What is Metabolomics?

## Slide 3
Metabolomics Workflow
Sample + Sample Preparation

## Slide 4
Metabolomics Workflow
Sample + Sample Preparation
Data Collection

## Slide 5
Metabolomics Workflow
Sample + Sample Preparation
Data Collection
Data Processing

## Slide 6
Metabolomics Workflow
Sample + Sample Preparation
Data Collection
Data Processing
Statistical Analysis

## Slide 7
Metabolomics Workflow
Sample + Sample Preparation
Data Collection
Data Processing
Statistical Analysis
Metabolite Identification

## Slide 8
Metabolomics Workflow
Sample + Sample Preparation
Data Collection
Data Processing
Statistical Analysis
Metabolite Identification
Molecular Networking

## Slide 9
Metabolomics Workflow
Sample + Sample Preparation
Data Collection
Data Processing
Statistical Analysis
Metabolite Identification
Molecular Networking
MODELS

## Slide 10
Metabolomics Workflow
Sample + Sample Preparation
Data Collection
Data Processing
Statistical Analysis
Metabolite Identification
Molecular Networking
MODELS
MODELS

## Slide 11
Metabolomics Workflow
Sample + Sample Preparation
Data Collection
Data Processing
Statistical Analysis
Metabolite Identification
Molecular Networking
MODELS
MODELS
MODELS

## Slide 12
Metabolomics Workflow
Sample + Sample Preparation
Data Collection
Data Processing
Statistical Analysis
Metabolite Identification
Molecular Networking
MODELS
MODELS
MODELS
MODELS

## Slide 13
Metabolomics Workflow
Sample + Sample Preparation
Data Collection
Data Processing
Statistical Analysis
Metabolite Identification
Molecular Networking
MODELS
MODELS
MODELS
MODELS
MODELS

## Slide 14
Metabolomics Workflow
Sample + Sample Preparation
Data Collection
Data Processing
Statistical Analysis
Metabolite Identification
Molecular Networking
MODELS
MODELS
MODELS
MODELS
MODELS

## Slide 15
Samples can be extremely varied, but standard option is blood, urine, etc – We use beer!
  No data protection issues
  Cheap and easily available
  Similar enough for method development
Metabolomics Mass Spectrometry Experiments

## Slide 16
Samples can be extremely varied, but standard option is blood, urine, etc – We use beer!
  No data protection issues
  Cheap and easily available
  Similar enough for method development
Metabolomics Mass Spectrometry Experiments
Ionisation

## Slide 17
Samples can be extremely varied, but standard option is blood, urine, etc – We use beer!
  No data protection issues
  Cheap and easily available
  Similar enough for method development
Metabolomics Mass Spectrometry Experiments
Mass Spectrometer
Ionisation

## Slide 18
Samples can be extremely varied, but standard option is blood, urine, etc – We use beer!
  No data protection issues
  Cheap and easily available
  Similar enough for method development
Metabolomics Mass Spectrometry Experiments
m/z
Intensity
Mass Spectrometer
Ionisation

## Slide 19
Sample
Sample fraction, collected in small time period
MS
Mass (per charge)
Chromatographic retention time
Chromatographic peaks
retention time
intensity
scans
LC-MS/MS

## Slide 20
MS1 scan
Measures mass (per charge), and intensity (how many copies of the molecule)
Scan also has an associated retention time
mass isn’t enough to identify the molecule
Scan Types – MS1

## Slide 21
Fragmentation: smashing up a molecule
MS
MS2 spectra can be used as a molecular fingerprint to identify molecules
Spectra are compared against a database of spectra for known molecules
Scan Types – MS2

## Slide 22
Sample + Sample Preparation
Data Collection
Data Processing
Statistical Analysis
Metabolite Identification
Molecular Networking
MODELS
MODELS
MODELS
MODELS
MODELS
How can Digital Twins help?

## Slide 23
Data Collection
MODELS
How can Digital Twins help?

## Slide 24
Data Collection
MODELS
How can Digital Twins help?

## Slide 25
Costs of Mass Spec: £1-2 million
Cost of yearly servicing: ~£100-200k
Cost to use Mass Spec per day: £2,000-2,500
Limited samples
Limited availability to use Mass Spec
What stops us building new models?

## Slide 26
What if we make a Digital Twin of a Mass Spectrometer?
How can Digital Twins help?

## Slide 27
ViMMS fully controls scan specifications in real time
Cruicially, experiments can be ran via computer simulations rather than on a real MS
Some Applications of ViMMS
  Evaluation of existing methods and settings
  Develop, evaluate and test new methods
  Control MS in real time via an API
  Evaluate current tools
What is the point of ViMMS?

## Slide 28
ViMMS has two environments
  Simulated (blue)
  Real (green)
How does ViMMS work?

## Slide 29
Construct peaks from previously observed data
Take average scan timings from previous data
How do the simulations work?

## Slide 30
The real experiments works in exactly the same way except using a sample rather than simulated ViMMS chemicals
How do the real experiments work?

## Slide 31
Controllers remain consistent across simulated and real experiments
Controlling the Scans

## Slide 32
The simulator uses the virtual mass spectrometer digital twin
The Mass Spectrometer

## Slide 33
The real mass spectrometer is used for the real experiments
The controller code is linked to the real mass spec via C# bridging code
Crucially:
The controllers remain the same
The bridging code is the same for all methods
The Mass Spectrometer

## Slide 34
We can use ViMMS to optimise our parameters in simulation before using the same controller on real samples
Unknown
Simulated Results
Controller
Optimising Data Acquisition Parameters

## Slide 35
We can use ViMMS to optimise our parameters in simulation before using the same controller on real samples
Unknown
Simulated Results
Optimised
Controller
Optimising Data Acquisition Parameters

## Slide 36
We can use ViMMS to optimise our parameters in simulation before using the same controller on real samples
Unknown
Simulated Results
Optimised
Controller
Controller
Optimising Data Acquisition Parameters

## Slide 37
We can use ViMMS to optimise our parameters in simulation before using the same controller on real samples
Optimising Data Acquisition Parameters
Unknown
Simulated Results
Optimised
Real Results
Controller
Controller

## Slide 38
Optimising Data Acquisition Parameters
To prove this strategy actually works, we full tested it across a number of methods

## Slide 39
Optimising DDA acquisition
Prototype
Controller
Simulated Results
We can use a similar strategy to design new controllers
An additional debugging and design step is added at the start

## Slide 40
Optimising DDA acquisition
Prototype
Controller
Simulated Results
Controller
We can use a similar strategy to design new controllers
An additional debugging and design step is added at the start

## Slide 41
Optimising DDA acquisition
Unknown
Simulated Results
Prototype
Controller
Simulated Results
Controller
We can use a similar strategy to design new controllers
An additional debugging and design step is added at the start

## Slide 42
Optimising DDA acquisition
Unknown
Simulated Results
Optimised
Prototype
Controller
Simulated Results
Controller
We can use a similar strategy to design new controllers
An additional debugging and design step is added at the start

## Slide 43
Optimising DDA acquisition
Unknown
Simulated Results
Optimised
Prototype
Controller
Controller
Simulated Results
Controller
We can use a similar strategy to design new controllers
An additional debugging and design step is added at the start

## Slide 44
Optimising DDA acquisition
Unknown
Simulated Results
Optimised
Prototype
Controller
Controller
Simulated Results
Real Results
Controller
We can use a similar strategy to design new controllers
An additional debugging and design step is added at the start

## Slide 45
Our New Methods

## Slide 46
We see an almost 50% improvement in results
Real Experimental Validation

## Slide 47
New Methods for Multiple Samples
We can similarly extend the concept to more advanced controllers, although the improvement is less drastic

## Slide 48
We can similarly implement other methods and test them
Evaluating Existing Methods

## Slide 49
We test other types of methods, as well as models for evaluating them
Evaluating a Different Acquisition Method

## Slide 50
Additional Parameter Optimisation

## Slide 51
Big thank you to all my collaborators:
  University of Glasgow: Joe Wandy, Rónán Daly, Simon Rogers, Ross McBride, Kevin Bryson, Stefan Weidt, Nikolaos Terzis, Alice Miller
  Wageningen University: Justin J.J. van der Hooft
Ideas for ViMMS or any further questions
  Email: vinny.davies@glasgow.ac.uk
  Twitter: vinny_davies89
Slides available at:
  https://github.com/vinnydavies/presentations
Any questions?