## Slide 1
Statistical and machine learning models for resolving metabolomics spectra
Dr Vinny Davies, University of Glasgow
Joint work with Nikolaos Terzis, Andrew Elliott, Rónán Daly, Joe Wandy, Justin JJ van der Hooft

## Slide 2
Metabolomics is the "systematic study of the unique chemical fingerprints that specific cellular processes leave behind", the study of their small-molecule metabolite profiles.
Basically, we are trying to identify all the metabolites in a particular sample
What is Metabolomics?

## Slide 3
Metabolomics Workflow
Sample + Sample Preparation

## Slide 4
Metabolomics Workflow
Sample + Sample Preparation
Data Collection

## Slide 5
Metabolomics Workflow
Sample + Sample Preparation
Data Collection
Data Processing

## Slide 6
Metabolomics Workflow
Sample + Sample Preparation
Data Collection
Data Processing
Statistical Analysis
Metabolite Identification
Molecular Networking

## Slide 7
Samples can be extremely varied, but standard option is blood, urine, etc – We use beer!
  No data protection issues
  Cheap and easily available
  Similar enough for method development
Metabolomics Mass Spectrometry Experiments

## Slide 8
Samples can be extremely varied, but standard option is blood, urine, etc – We use beer!
  No data protection issues
  Cheap and easily available
  Similar enough for method development
Metabolomics Mass Spectrometry Experiments
Ionisation

## Slide 9
Samples can be extremely varied, but standard option is blood, urine, etc – We use beer!
  No data protection issues
  Cheap and easily available
  Similar enough for method development
Metabolomics Mass Spectrometry Experiments
Mass Spectrometer
Ionisation

## Slide 10
Samples can be extremely varied, but standard option is blood, urine, etc – We use beer!
  No data protection issues
  Cheap and easily available
  Similar enough for method development
Metabolomics Mass Spectrometry Experiments
m/z
Intensity
Mass Spectrometer
Ionisation

## Slide 11
Sample
Sample fraction, collected in small time period
MS
Mass (per charge)
Chromatographic retention time
Chromatographic peaks
retention time
intensity
scans
LC-MS/MS

## Slide 12
MS1 Scans
m/z
Intensity
MS1 scans show us the amount of each metabolite at any given time,
For each metabolite (colour), we record the intensity, , for given block,
  We do not observe all metabolites at each scan (hence , ,

## Slide 13
MS2 Scans
m/z
Intensity
MS2 scans allow us to break down the metabolites, so that we can identify them – this can be done for single metabolites (DDA)
m/z
Intensity

## Slide 14
MS2 Scans
m/z
Intensity
This becomes more difficult in our experiments where we do it for multiple metabolites (DIA)
m/z
Intensity

## Slide 15
MS2 Scans
m/z
Intensity
This becomes more difficult in our experiments where we do it for multiple metabolites (DIA)
m/z
Intensity
What we actually see (no colours)

## Slide 16
Our Aim
m/z
Intensity
m/z
Intensity
m/z
Intensity
m/z
Intensity

## Slide 17
How do we do this?
m/z
Intensity
m/z
Intensity
Link all our MS1 scans to all our MS2 scans
  1000-2000 of each scan type
  2000-5000 metabolite (each observed over 10-100 MS1/MS2 scans)
  50,000-100,000 fragments (each observed over 10-100 MS2 scans

## Slide 18
Data Format – Response
m/z
Intensity
MS1 data is split into bins based on m/z
  m/z stays relatively consistent
Maximum value within each bin is taken for each scan, , giving
Combining all the scans we can then get
We will then fit models for each bin using

## Slide 19
Data Format – Covariates
Peaks are identified using all the MS1 scans
m/z
Intensity

## Slide 20
Data Format – Covariates
Peaks are identified using all the MS1 scans
m/z
Intensity

## Slide 21
Data Format – Covariates
m/z
Intensity
Each peak, , is bound within a box
For each MS1 scan, , the values of each covariates is given by where:
  if is not present at time,
  takes the intensity of if it is present
For each scan we therefore have , which then gives us
We use the same base for each response
  Covariates that are 0 for all are filtered

## Slide 22
Regression Models
We can then fit regression models for each using the filtered version of
  Filtering ensures
Significance or selection is different for each of the models
Selection of covariate in model indicates there is a link between the metabolite observed in the MS1 scans and the fragment in the MS2 scans

## Slide 23
Reconstruction of Spectra
We estimate the spectra at the maximum intensity of its associated metabolite
We estimate the fragment intensity of each bin for each as:
where will often be 0
We can then 0-1 normalize all and we can compare against our true spectra

## Slide 24
Evaluation via a Digital Twin
We initially evaluated our method (MSDeconvolve) on our digital twin (simulator) called ViMMS
ViMMS can simulate full LC-MS/MS experiments and
ViMMS has been shown to be able to replicate existing methods

## Slide 25
Evaluation via a Digital Twin
Results on the digital twin are extremely encouraging

## Slide 26
Evaluation via real data
Current thoughts
  “Maybe we should submit it to Nature rather than Nature Methods”
  “We have tested ViMMS extensively and it's always been reliable, so surely it’ll be the same for this…”
Let’s see…

## Slide 27
Evaluation via real data
Ah…

## Slide 28
Evaluation via real data
Ah…
Maybe its still fixable?

## Slide 29
Comparison of Methods
We compared several readily available methods
Requires relatively fast methods, as need to fit around 1000 models and people would expect results in around 15mins

## Slide 30
Baseline Noise Removal
We tried removing the baseline noise

## Slide 31
Constrained Covariates
Constraining the model coefficient to be positive gave a small increase in performance

## Slide 32
Ensemble Approach
Combining multiple versions of MSDeconvolve with MS-DIAL via an Ensemble approach gave a small improvement in performance
Different thresholds were used to compare the performance

## Slide 33
Conclusions
The performance of MSDeconvolve is not particularly good
Its performance on the simulated data suggests that the concept makes sense, but more work is needed
Likely the noise and data complexity is overwhelming the model
Future Plans
Remove the dependence on peak picking
Add additional constraints based on prior knowledge

## Slide 34: Thanks for Listening
Let me know if you have any questions
Or feel free to reach out at: Vinny.Davies@Glasgow.ac.uk
Slides available (soon) at:
https://github.com/vinnydavies/presentations