## Slide 1
ViMMS 2.0: A framework to develop, test and optimise fragmentation strategies in LC-MS metabolomics
Dr Vinny Davies

## Slide 2
ViMMS is a Virtual Metabolomics Mass Spectrometer
It allows you to simulate full metabolomics LC-MS/MS experiments
  MS1 and MS2 capabilities, with potential for MSN
ViMMS is implemented within Python and is full open source available at https://github.com/glasgowcompbio/vimms
ViMMS
Wandy, J., Davies, V., et al. (2019). In silico optimization of mass spectrometry fragmentation strategies in metabolomics. Metabolites.
Wandy, J., Davies, V., et al. (2022). ViMMS 2.0: A framework to develop, test and optimise fragmentation strategies in LC-MS metabolomics. JOSS.

## Slide 3
ViMMS fully controls scan specifications in real time and allows
Evaluation of existing methods and settings
Develop, evaluate and test new methods
Control MS in real time via an API
Evaluate current tools, e.g. MS-dial
Currently real time control is limited to Thermo Fisher machines with IAPI control
What is the point of ViMMS?

## Slide 4
ViMMS has two environments
  Simulated (blue)
  Real (green)
The virtual MS (Python code) and real MS (an actual instrument) are interchangeable
Controllers (which schedule scans) are identical in both environments
Samples are either real or virtual
How does ViMMS work?

## Slide 5
Take an mzml and construct Regions of Interest (ROIs)
ROIs are converted into ViMMS chemicals
How do the simulations work?

## Slide 6
Timings for MS1 and MS2 scans are taken directly from the mzml
MS2 spectra are fully synthetic, (e.g. we cannot get new real results)
Standard methods such as Top-N are implemented within ViMMS as controllers (these determine scans)
Results are extracted as mzmls and can analysed in terms of perfomance
How do the simulations work?

## Slide 7
The real experiments works in exactly the same way except using a sample rather than simulated ViMMS chemicals
How do the real experiments work?

## Slide 8
Controllers remain consistent across simulated and real experiments
Works through use of Thermo IAPI to control scans in real time (via Python and C++ bridging code)
We can use any ViMMS controller on real samples in this manner
How do the real experiments work?

## Slide 9
Optimise existing methods
Develop new single-sample DDA methods
Test / develop multi-sample DDA methods
Compare DDA and DIA
Develop new DIA deconvolution methods (ongoing)
Future plans: there are a lots of options. Suggestions very welcome!
What have we used ViMMS to do?

## Slide 10
A few different DDA methods are currently implemented within ViMMS
We can use the simulated environment to test different parameter settings on a previously collected sample
Advantage: No machine time or sample costs. Optimised performance for next DDA acquisition
Optimising DDA acquisition

## Slide 11
We compared performance of our ViMMS Top-N controller (simulated chemicals) vs machine Top-N (same real sample)
Results show simulations in ViMMS closely match the real performance
Optimising Top-N
Wandy, J., Davies, V., et al. (2019). In silico optimization of mass spectrometry fragmentation strategies in metabolomics. Metabolites.

## Slide 12
We can also develop new methods
We motivated our methods to avoid repeated fragmentation events (e.g. below)
We can then compare them against Top-N
Developing new DDA methods
Davies, V., et al. (2021). Rapid development of improved data-dependent acquisition strategies. Analytical chemistry.

## Slide 13
SmartROI constructs ROIs in real time
Uses rises and falls in intensity to determine if an MS2 scan is allowed
SmartROI

## Slide 14
WeightedDEW constructs a new type of Dynamic Exclusion Window (DEW)
WeightedDEW

## Slide 15
ViMMS allowed us to develop and debug these methods before ever using samples or machine time
We then optimised the parameters of the methods to maximise peak coverage (or any other metric you choose)
In-Silico Development in ViMMS

## Slide 16
We then tested them out in different simulated scenarios in ViMMS
Big increase in performance when there are a large number of metabolites (peaks)
In-Silico Validation in ViMMS

## Slide 17
We then tested the methods on real samples (beer and serum)
Results showed a 50%+ increase in performance
Real Experimental Validation

## Slide 18
Under the same principles, we can also develop multi-sample DDA methods and test existing ones, e.g. DsDA, MSplanner
What about multi sample DDA methods?

## Slide 19
TopNEXt is a modular framework for multi-sample acquisition
It scores possible MS2 scans based on previously observed scans in the current and previous samples
TopNEXt: Automated Exclusion
McBride, R., …, Davies, V., … et al. (2023). TopNEXt: Automatic DDA Exclusion Framework for Multi-Sample Mass Spectrometry Experiments.

## Slide 20
It contains a number of different options and can easily be extended
TopNEXt: Automated Exclusion
McBride, R., …, Davies, V., … et al. (2023). TopNEXt: Automatic DDA Exclusion Framework for Multi-Sample Mass Spectrometry Experiments.

## Slide 21
Beyond the framework, it also introduces the concept of (non-)overlap
It looks at how much a current ROI (black) overlaps with a previous ROI (blue) and scores it based on how much they overlap
The more it overlaps with a fragmented previous ROI, the lower it will be scored
There is also a version based on the intensity of the previous MS2 scans
Non-Overlap

## Slide 22
TopNEXt: Automated Exclusion

## Slide 23
TopNEXt: Automated Exclusion

## Slide 24
We can similarly implement DIA in ViMMS (and eventually TopNEXt)
What about DIA?

## Slide 25
We have implemented SWATH and AIF within ViMMS
Compared them against DDA
DIA vs DDA

## Slide 26
We can construct our own DIA methods or even hybrid DDA-DIA methods
Limitation appears to be the deconvolution
  Generally inflexible
  Low accuracy
  Overly correlated predicted spectra
ViMMS allows us to properly evaluate deconvolution and we have began designing our own method
  I see this as the immediate application of ViMMS
Bottleneck of DIA?
Wandy, J., ... & Davies, V. (2023). Simulated-to-real Benchmarking of Acquisition Methods in Metabolomics. bioRxiv.

## Slide 27
Big thank you to all my collaborators:
  University of Glasgow: Joe Wandy, Rónán Daly, Simon Rogers, Ross McBride, Kevin Bryson, Stefan Weidt, Nikolaos Terzis, Alice Miller
  Wageningen University: Justin J.J. van der Hooft
Ideas for ViMMS or any further questions
  Email: vinny.davies@glasgow.ac.uk
  Twitter: vinny_davies89
Slides available at:
  https://github.com/vinnydavies/presentations
Any questions?